CPSC 501 Assignment 4
Walter Joubert
10081472

All tests run against the same input files:
Dry: Sitar.wav
Impulse: l960taj_mahal_deep6.wav

Profiling: Done with gprof

Regression Testing: Used audiodiff to check that output were the same for each stage of optimization

BaseLine Run:
Timing reported by run: 465.827 seconds
Profiling :
Each sample counts as 0.01 seconds.
  % cumulative self self total
 time seconds seconds calls s/call s/call name
100.00 464.39 464.39 1 464.39 464.39 convolve(float*, int, float*, int, float*, int)
    0.00 464.39 0.00 2 0.00 0.00 read_wav(char const*, float*&)
    0.00 464.39 0.00 1 0.00 0.00 write_wav(char const*, float*&, int)

FFT (Untuned) Run:
Timing reported by run: 2.85979 seconds
Each sample counts as 0.01 seconds.
  % cumulative self self total
 time seconds seconds calls s/call s/call name
 97.22 2.79 2.79 3 0.93 0.93 four1(double*, int, int)
   2.79 2.87 0.08 1 0.08 2.87 convolve(double*, int, double*, int, double*&, int)
   0.00 2.87 0.00 2 0.00 0.00 read_wav(char const*, double*&)
   0.00 2.87 0.00 1 0.00 0.00 write_wav(char const*, double*&, int)

Majority of time is spent running four1 so must optimizations should be preformed here. The rest of the time is spent in the convolve function therefore some optimization can be preformed here as well.

Testing each code tuning: Verified that change lowered runtime and the output file diffed with an untuned output file is identical (using audiodiff).

FFT (Code Tuned) Run:
1) Strength Reduction:
New:
// Load data into x_complex to be used in fft
for (int i = 0; i < input_size; i++)
x_complex[i + i] = input_signal[i];

// Load data into h_complex to be used in fft
for (int i = 0; i < impulse_size; i++)
h_complex[i + i] = impulse_response[i];

Old:
// Load data into x_complex to be used in fft
for (int i = 0; i < input_size; i++)
x_complex[2 * i] = input_signal[i];

// Load data into h_complex to be used in fft
for (int i = 0; i < impulse_size; i++)
h_complex[2 * i] = impulse_response[i];

Timing reported by run: 2.32167 seconds
Each sample counts as 0.01 seconds.
  % cumulative self self total
 time seconds seconds calls s/call s/call name
 96.55 2.24 2.24 3 0.75 0.75 four1(double*, int, int)
   3.45 2.32 0.08 1 0.08 2.32 convolve(double*, int, double*, int, double*&, int)
   0.00 2.32 0.00 2 0.00 0.00 read_wav(char const*, double*&)
   0.00 2.32 0.00 1 0.00 0.00 write_wav(char const*, double*&, int)

2) Fusion:
New:
for (int i = 0; i < double_pow2; i++)
{
x_complex[i] = 0.0;
h_complex[i] = 0.0;
y_complex[i] = 0.0;
}

Old:
for (int i = 0; i < double_pow2; i++)
x_complex[i] = 0.0;
for (int i = 0; i < double_pow2; i++)
h_complex[i] = 0.0;
for (int i = 0; i < double_pow2; i++)
y_complex[i] = 0.0;

Timing reported by run: 2.12303 seconds
Each sample counts as 0.01 seconds.
  % cumulative self self total
 time seconds seconds calls s/call s/call name
97.66 2.08 2.08 3 0.69 0.69 four1(double*, int, int)
  1.88 2.12 0.04 1 0.04 2.12 convolve(double*, int, double*, int, double*&, int)
  0.00 2.13 0.00 2 0.00 0.00 read_wav(char const*, double*&)
0.00 2.13 0.00 1 0.00 0.00 write_wav(char const*, double*&, int)

3) Partial Unrolling:
New:
for (int i = 0; i < double_pow2 - 2; i+=3)
{
x_complex[i] = 0.0;
x_complex[i + 1] = 0.0;
x_complex[i + 2] = 0.0;
h_complex[i] = 0.0;
h_complex[i + 1] = 0.0;
h_complex[i + 2] = 0.0;
y_complex[i] = 0.0;
y_complex[i + 1] = 0.0;
y_complex[i + 2] = 0.0;

if (i == double_pow2 - 2) {
x_complex[i - 1] = 0.0;
x_complex[i - 2] = 0.0;
h_complex[i - 1] = 0.0;
h_complex[i - 2] = 0.0;
y_complex[i - 1] = 0.0;
y_complex[i - 2] = 0.0;
} else if (i == double_pow2 - 1) {
x_complex[i - 1] = 0.0;
h_complex[i - 1] = 0.0;
y_complex[i - 1] = 0.0;
}
}

Old:
for (int i = 0; i < double_pow2; i++)
{
x_complex[i] = 0.0;
h_complex[i] = 0.0;
y_complex[i] = 0.0;
}

Timing reported by run: 2.10386 seconds
Each sample counts as 0.01 seconds.
  % cumulative self self total
 time seconds seconds calls s/call s/call name
97.62 2.05 2.05 3 0.68 0.68 four1(double*, int, int)
  2.38 2.10 0.05 1 0.05 2.10 convolve(double*, int, double*, int, double*&, int)
  0.00 2.10 0.00 2 0.00 0.00 read_wav(char const*, double*&)
  0.00 2.10 0.00 1 0.00 0.00 write_wav(char const*, double*&, int)